SSS CONTACT & CIRCUIT BOARD CLEANER IV

Description:  This premium precision cleaner provides a solution for your most demanding industrial and electronics maintenance problems. The completely nonflammable formula utilizes the latest innovations in HFC chemistry to create a high purity, nonresidue, fast dry formula, that is completely plastics safe. Neoprene W., Buna N, Buna S, Silicone rubber, Butyl, Natural rubber, Thiokol FA, Viton A, Adiprene L, Nordel, Delrin resin, Zytel, Nylon, Teflon, PVC, Polyurethane, Styrene, Polystyrene, Polypropylene, ABS, and more are not affected by this product. In addition, it is nonconductive to over 20 KV per ASTM D-877 and will not cause “freeze out” or attract moisture when used as directed. It quickly and easily removes dirt, dust, light oils, flux, and other deposits from contacts, circuit boards, relays, switches, solder joints, and other electronics devices. An excellent choice for the maintenance of all electronic or electrical devices in industry.

Directions:  WIDE AREA CLEANING: Shake can well before using. Hold can about 6-8 inches from surface to be cleaned. Aim at desired area and spray using a sweeping side to side motion.  Allow to air dry.  PRECISION CLEANING: Insert the extension tube firmly into the nozzle opening. Hold can about 2-3 inches from surface to be cleaned. Aim and spray until clean. Allow to air dry.

Health Hazard Data:  Contents under pressure. Do not puncture or incinerate container. Do not expose to heat or store at temperatures above 120(F. KEEP OUT OF REACH OF CHILDREN.

Spill Or Leakage Procedures:  Extinguish ignition or combustion sources. Keep up wind of spill. Stop leak.  Aerosol cans when vented to atmospheric pressure through normal use, pose no disposal hazard.

Product Specifications:

Wt./16oz. can:	10 Ounces

Classification:	Aerosol Contact & Circuit Board Cleaner

General Appearance:	Clear Mist Spray

Color:	Colorless

Odor:	Ethereal Solvent

pH:	N/A

Vapor Pressure At 70°F:	50-60 psig

Spray Pattern:	Forceful Mist

Flammability:	Not flammable per CPSC Flame Projection Test

NFPA Code 30B:		Level 1