SSS SAFETY SOLVENT

Description:  This is a highly concentrated solvent designed to remove dirt, grease, oil and grime from metallic and non-metallic surfaces. Cleaning is quick and simple without the danger of injury to working parts. This solvent is ideally suited for use on electric motors (even while running), electronic equipment, ignition systems, typewriters, computers, generators, power tools, etc. It is nonflammable and nonconductive so it will not short motors, generators, other electrical equipment, or increase fire hazard.  It easily removes grease and tar, adhesive marks, crayon, lipstick, chewing gum, ink and fresh paint. It is excellent for removing these spots from upholstery fabrics, rugs, clothing, painted surfaces, metals and other surfaces.  WARNING: Prolonged contact with aluminum will cause discoloration. While safe to use on most plastics the solvent in this product will soften and eventually dissolve polystyrenes (such as styrofoam) and polycarbonates (such as Lexan, Merlan, etc.) If unsure of surface composition, test in an inconspicuous area. This product is for use by trained professionals only. NOT FOR RETAIL SALE.

Directions:  Keep actuator pointed towards dot on valve cup. Remove cap and spray generously over the surface to be cleaned until it is completely wet. Allow the solvent to set for a minute, then wipe or rinse off with a second spray. On heavily encrusted areas, use a brush. This solvent is non-flammable and non-conductive, so it can be used while motors and equipment are operating.

Health Hazard Data:  Vapor harmful. Contains Perchloroethylene and Trichloroethylene. Use with adequate ventilation to keep exposure levels below the 25 parts per million O.S.H.A. permissible exposure limit (PEL) during an eight hour period (time weighted average). Consult the product material safety data sheet for additional information regarding exposure concerns. Avoid inhalation of spray mist or vapors. If overcome by fumes, remove victim to fresh air. Resuscitate if necessary. Get medical attention. Avoid contact with eyes and skin. In case of eye contact, flush immediately with plenty of water and continue for 15 minutes. If discomfort persists, see a physician. Contents are under pressure. Do not puncture or incinerate container. Do not expose to heat or store at temperatures above 120°F. WARNING: This product contains a chemical or chemicals known to the State of California to cause cancer. KEEP OUT OF REACH OF CHILDREN.

Spill Or Leakage Procedures:  Allow to evaporate with adequate ventilation. Do not flush to sewer. Aerosol cans when vented to atmospheric pressure through normal use pose no disposal problem.

Product Specifications:

Wt./20oz. can:	20 Ounces

USDA Category:	K2

Classification:	Aerosol Cleaning Solvent

General Appearance:	Clear

Color:	Colorless

Odor:	Chlorinated Solvent

pH:	N/A

Vapor Pressure At 70°F:	85 - 100 psig

Spray Pattern:	Blasting Stream

Flammability:	Not flammable per CPSC Flame Projection Test

NFPA Code 30B:	Level 1